void main (void){

#include <msp430g2553.h>

#define	M	50000 //contando o tempo
#define	led_do	BIT0
#define	led_re	BIT1
#define	led_mi	BIT2
#define	led_fa	BIT3
#define	led_sol	BIT4
#define	led_la	BIT5
#define	led_si	BIT6
#define	motor	BIT7

WDTCTL = WDTPW|WDTHOLD; // Desliga WDT
P1OUT = 0; // zerando saída
P1DIR |= 0xFF; // direcionando a saída de bits <0-7>, 255 em decimal

for(;;){
if (264 <real[i] < 297){ //frequencia_do

P1OUT |= led_do| motor; // liga o led_do e o motor
// controle da tensão

else if (297 <real[i] < 330 ){ //frequencia_re

P1OUT |= led_re| motor; // liga o led_re e o motor
// controle da tensão

else if (330 <real[i] < 352 ){ //frequencia_mi

P1OUT |= led_mi| motor; // liga o led_mi e o motor
// controle da tensão

else if (352 <real[i] < 396 ){ //frequencia_fa

P1OUT |= led_fa| motor; // liga o led_fa e o motor
// controle de tensão

else if (396 <real[i] < 440 ){ //frequencia_sol

P1OUT |= led_sol| motor; // liga o led_sol e motor
//controle de tensão

else if (440 <real[i] < 495 ){ //frequencia_la

P1OUT |= led_la| motor // liga o led_do e o motor
// controle de tensão

else if (495 <real[i] < 528 ){ //frequencia_si

P1OUT |= led_si| motor // liga o led_si e o motor
//controle de tensão

}
}
}
}
}
}
}

}//end loop infinito
}//end main

FUNÇÃO

#include "fix_fft.h"

int real[nPts];
int imag[nPts];
int sampleInterval;

void setup()

{
  Serial.begin(115200);
  delay(500); //give time for serial monitor to start up in Energia
  analogReadResolution(ANALOG_RESOLUTION);

  //****************** interval calculation *******************************

  int unCorrectedSampleInterval = 500000/hiFreq;
  long startTime = micros();
  for(int i = 0; i < nPts; i++){ // determine total actual time for uncorrected interval
    real[i] = analogRead(ANALOG_IN);
    delayMicroseconds(unCorrectedSampleInterval); // unadjusted sample interval
  }
  long endTime = micros();
  int totalTime = (int)(endTime - startTime);
  int expectedTime = nPts * unCorrectedSampleInterval;
  int errorTime = totalTime - expectedTime;
  sampleInterval = unCorrectedSampleInterval - errorTime/nPts;

}

void loop()
{
  int i;
  long startTime = micros();
  for (i=0; i<nPts; i++) { // read ADC pin nPts times at hiFreq kHz
    real[i] = analogRead(ANALOG_IN);
    delayMicroseconds(sampleInterval); // adjusted sample interval
  }

  for( i=0; i<nPts; i++) imag[i] = 0; // clear imaginary array

  fix_fft(real, imag, LOG2N, 0); // perform fft on sampled points in real[i]

  for ( i = 0; i < nPts/2; i++) //get the power magnitude in each bin
    {
      real[i] =sqrt((long)real[i] * (long)real[i] + (long)imag[i] * (long)imag[i]);
    }

  if (DEBUG) {
    long endTime = micros();
    Serial.print ("\nSampling time : ");
    Serial.print (endTime - startTime);
    Serial.println (" micro seconds");
    // find the peak
    int peakHz = 0;
    int peaki = 0;
    for (i = 1; i < nPts/2; i++) { // bin 0 holds the summation - not peak
      if (real[i] > peakHz) {
        peakHz = real[i];
        peaki = i;
      }
    }
    peakHz = (peaki * FREQ_RESOLUTION) - FREQ_RESOLUTION/2;
    Serial.print ("Peak frequency : ");
    Serial.println (peakHz);
    Serial.println ("");
  }

  while(1);
}